HIGHLY ELECTRIC CO., LTD

ES-SERIES EMERGENCY STOP SWITCH

- Specification

| Standards | EN60947-5-1 |
| --- | --- |
| Safety Contacts | 1 N.C. direct opening action |
| Auxiliary Contact | 1 N.O. |
| Designation / Utilization Category A300 / AC-15 Q300 / DC-13 |  |
|  | Ue(V): 120 240 |
|  | Ie (A): 6 3 |
|  | Ue(V): 125 250 |
|  | Ie (A): 0.55 0.27 |
| Dielectric Voltage | 2000 V |
| Thermal Current (lth) | 10A |
| Insulation Resistance | 100M min. (500VAC) |
| Contact Resistance | 25m max. |
| Safety Contact gap | >2 × 2 mm (0.078in) |
| Protection | IP 40 |
| Case Material | UL approved A.B.S. copolymers |
| Pollution Degree | 3 |
| Operated Setting | Flexible Rope |
| Min. Direct Opening Travel | 1.2mm |
| Min. Direct Opening Force | 6N |
| Max. Actuating Travel | >7.0mm |
| Positive opening Travel | 2.2mm |
| Positive opening force | 10N |

- Order guide

ES-R-□

■ Mounting condition

Installation Instructions

Installation must be in accordance with the following steps and stated specifications and should be carried out by suitably competent personnel.

| 1. Mounting holes |
| --- |
| 2. Mounting example Type A This example is for reference only | Type B This example is for reference only |
| 3. Additional requirements for colour coding Yellow shall indicate the correct setting of actuated position. |
| WARNING: Do not defeat, tamper, remove or bypass this unit. Severe injury to personnel could result. |

■ Operating Characteristic

| Maximum Length of Rope | 1.5 Meter |
| --- | --- |
| Correct Tension of Rope | 5% |
| Distance Between Supports | 1.5 Meter |
| Perpendicular Deflection of Rope | < 400mm |
| Perpendicular Pulling Force applied to the rope | 10N |
| Direct Opening Travel | 2.6mm |

■ CAUTION:

Before allowing normal machine use by an operator, check that when the rope is pulled in any direction at any position, the machine power is isolated and the reset mechanism on switch latches in.

The rope should be inspected at regular intervals for any signs of damage or wear.

Dimensions

Type A

Type B

- Recommended Pull Angle

- Soldering the Wire

Release four screws and removing lid, then taken the switch and rubber out.

The wire to pierce hole in the rubber. Soldered the wires with terminal together. The wire must be hooked before soldering. Restore the switch and rubber after Soldering.

Restore the lid and four screws. The maximal enclosure fixing screw torque is 0.3NM.

CAUTION:

Be sure to use electrical wires that are a size appropriate for the applied voltage and carry current.

Perform soldering according to the conditions provided below. If the soldering is not properly performed, the lead wires will become detached, resulting in short-circuits.

1. Hand soldering: 30 W, within 5 s

2. Dip soldering: 240°C, within 3 s

Wait for one minute after soldering before exerting any external force on the solder.

Use non-corrosive resin fluid as the flux.

Make sure that the electric cord is wired so that it does not touch the Unit. If the electric cord touches the Unit, then electric wires with a heat resistance of 100°C min. must be used.

After wiring the Switch, maintain an appropriate clearance and creepage distance.

- Artwork of rating label

# Text boxes

Panel

Mounting hole

A: Without mounting holes type on housing

B: Mounting holes type on housing